## Slide 1: SAMPLING
ACT / ACG Training
General
Notes: INSERT NOTES HERE

## Slide 2: Objectives
Answer – What is Sampling?
Cover an introduction to Sampling Services

## Slide 3: Sampling Service
A portion obtained from a lot of grain or commodity, by official inspection personnel, that is representative of the lot
Obtaining a representative sample from a lot of grain is the MOST important part of inspection
If the sample is not representative, the inspector’s final grade will not reflect the true grade of the lot

## Slide 4: Representative Samples
To be representative a sample must be:
  Obtained by Official Personnel
    Using approved equipment and procedures
  Of Prescribed size
  Handled securely
  Protected from:
    Manipulation
    Substitution
    Careless Handling

## Slide 5: Sampling
Official Sampling Devices:
    Probe
    Pelican
    Ellis Cup
    Diverter Type Sampler (D/T)

## Slide 6: Ship Sampling
Sampling rates are determined by lot size
Applicants (elevators) determine lot size and communicate those through Load Orders
Load Orders are the Applicant’s contract requirements for the lot to be loaded

## Slide 7: Establishing Sublot Size
Sublot size determines the frequency of inspection in which official personnel examine the sublot samples
The applicant may establish the sublot size
Number and size of sublots in a lot are declared by the Load Order
Applicants may not request a change to the sublot size once the sublot size is established and loading begins
Sublots must be reasonably uniform in size

## Slide 8: Establishing Sublot Size

## Slide 9: Ship - Uniformity Criteria
Samples are continuously obtained and examined during the loading to determine uniformity
Official personnel are responsible for determining when subsamples, component samples, and sublot samples are analyzed

## Slide 10: Ship - Uniformity Criteria
Subsamples:
  Represent up to 5,000 bushels
Component samples:
  Comprised of Subsamples
  Minimum 10,000 bushels - Maximum 40,000 bushels
  Examined for insects, heating, odor, DLQ, and unusual conditions
Sublot samples:
  Comprised of Component samples that are uniform in kind and condition

## Slide 11: Component and Sublot Samples

## Slide 12: D/T Sampling Before Loading
Prior to loading, and otherwise directed by your supervisor, examine the safety, security, integrity, and representativeness of the sampling system.
Check inside and around the Pelican of the Primary for objects which may restrict grain flow and for obvious changes to the pelican width.
Observe the Primary pelican stopping completely against the dust seals and is shielded from the grain flow.
Inspect the condition of the dust seals on the Primary housing to ensure unwanted grain, dust, or debris from entering the sampling system.

## Slide 13: D/T Sampling Before Loading
Observe pelican moving to ensure it is traversing at an even speed, as close to 0.5 meter/sec (20 inches/sec).
Secure access points such as: primary, secondary, and sample tubing by using approved FGIS seals or FGIS locks.
Record seal numbers according to local procedures.
Ensure sampler controls are operational and the timer is at the proper setting.
Immediately notify your supervisor to alert facility personnel of any malfunctions.
Corrections must be made before loading starts.

## Slide 14: D/T Sampling During Loading
After the Carrier is FIT-TO-LOAD and the sampling system is satisfactory, follow local procedures.
Monitor the operation of the sampling system from your work station by watching sampler controls and the amount of grain being sampled.
Empty the collection box after each subsample and examine for off-odors and non-uniformity condition.
Perform infestations checks and non-uniformity checks by using an 8/64 inch round hole sieve for Corn. For ALL OTHER Grains use an 0.64-inch by 3/8-inch oblong sieve.
Examine the contents of the TOP and BOTTOM pans for infestation, unknown foreign substance, crotalaria, etc.
When grain of inferior condition is found notify the facility manager and keep the sub-sample separate. Do not separate sub-samples for infestation. When grain is NOT of inferior condition, add it to the whole sample.

## Slide 15: D/T Sampling During Loading
Grain is considered INFESTED when the total number of live insects from subsamples within a specified component which meets or exceeds the amount listed below.
Wheat, Rye, Triticale
ALL OTHER GRAINS
Monitor belt or flow for objects too large to enter the D/T.
Observe loading to determine if FM is added or recombined and there is no blending of other grains into the grain being loaded.
Perform routine security checks of sampling system.
Secure samples during any absences, i.e. lunch breaks, security checks, belts checks etc.
Document activities according to local established procedures.

## Slide 16: Safety
Safety is mandatory!
Be aware of your surroundings
  Be aware of tight spaces, moving machinery, and do not enter toxic/low-oxygen atmospheres
Use personal protective equipment (PPE)
  Hard hat, safety/reflective vest, and gloves
Be familiar with general emergency procedures
and facility/local emergency procedure
PROBEY (Smokey’s brother) Says:
  “Only you can ensure safety”
If you see something that you suspect is a dangerous situation, say something to a supervisor and elevator personnel!
Probey

## Slide 17: Standards of Fitness
A stowage area must be suitable for storing or carrying grain or commodities
Suitable stowage area is:
  clean
  dry
  free of infestation, rodents, toxic substances
  foreign odor

## Slide 18: Standard of Fitness
Rust / Paint Scale –
  25 square feet single area/ 100 square feet aggregate – ships, barges
  4 square feet single area or aggregate – railcars, trucks, or other
Previous Cargo – Not allowed
  Such as – fertilizer, coal, oil residue, cement, old grain
Unsanitary Conditions – Not allowed
  Such as – animal filth, sewage, or any other condition
Dryness – No standing water or puddles
Free from infestation, rodents, toxic substances, odor
Other conditions that would make storage questionable

## Slide 19: Procedure
Check entire carrier for all standards of fitness
Point out conditions that do not meet standards to the applicant
  Minor corrections can be made on the fly by applicant
  Items needing significant correction = unfit declaration
Document results on the work record (pass or fail)

## Slide 20: Summary
This presentation covered an introduction to Stowage Examination Services

## Slide 21: Conclusion / References
Questions? See your trainer or FOM
References for clarification
  See FGIS Program Directive 9180.48
  FGIS Policy Bulletins #261 and #262